## Slide 1: Chapter 1 Computer System Overview
Ninth Edition
By William Stallings
Operating Systems: Internals and Design Principles
Notes: “Operating Systems: Internal and Design Principles”, 9/e, by William Stallings, Chapter 1 “Computer System Overview”.

## Slide 2: Operating System
Exploits the hardware resources of one or more processors
Provides a set of services to system users
Manages secondary memory and I/O devices
Notes: An operating system (OS) exploits the hardware resources of one or more processors to provide a set of services to system users. The OS also manages secondary memory and I/O (input/output) devices on behalf of its users. Accordingly, it is important to have some understanding of the underlying computer system hardware before we begin our examination of operating systems.
This chapter provides an overview of computer system hardware. In most areas,
the survey is brief, as it is assumed that the reader is familiar with this subject. However,
several areas are covered in some detail because of their importance to topics
covered later in the book. Further topics are covered in Appendix C. For a more
detailed treatment, see [STAL16a].

## Slide 3: Basic Elements
Processor
Main Memory
I/O Modules
System Bus
Notes: At a top level, a computer consists of processor, memory, and I/O components, with one or more modules of each type. These components are interconnected in some fashion to achieve the main function of the computer, which is to execute programs. Thus, there are four main structural elements:
Processor
I/O Modules
Main Memory
System Bus

## Slide 4: Processor
Controls the operation of the computer
Performs the data processing functions
Referred to as the Central Processing Unit (CPU)
Notes: Processor : Controls the operation of the computer and performs its data processing functions. When there is only one processor, it is often referred to as the central processing unit (CPU).

## Slide 5: Main Memory
Stores data and programs
Typically volatile
  Contents of the memory is lost when the computer is shut down
Referred to as real memory or primary memory
Notes: Main memory : Stores data and programs. This memory is typically volatile; that is, when the computer is shut down, the contents of the memory are lost. In contrast, the contents of disk memory are retained even when the computer system is shut down. Main memory is also referred to as real memory or primary memory.

## Slide 6: I/O Modules
Move data between the computer and its external environment
Secondary memory devices (e.g. disks)
Communications equipment
Terminals
Notes: I/O modules : Move data between the computer and its external environment. The external environment consists of a variety of devices, including secondary
memory devices (e.g., disks), communications equipment, and terminals.

## Slide 7: System Bus
  Provides for communication among processors, main memory, and I/O modules
Notes: System bus : Provides for communication among processors, main memory, and I/O modules.

## Slide 8
Notes: Figure 1.1 depicts these top-level components. One of the processor’s functions is to exchange data with memory. For this purpose, it typically makes use of two internal (to the processor) registers: a memory address register (MAR), which specifies the address in memory for the next read or write; and a memory buffer register (MBR), which contains the data to be written into memory or which receives the data read from memory. Similarly, an I/O address register (I/OAR) specifies a particular I/O device. An I/O buffer register (I/OBR) is used for the exchange of data between an I/O module and the processor.
A memory module consists of a set of locations, defined by sequentially numbered addresses. Each location contains a bit pattern that can be interpreted as either an instruction or data. An I/O module transfers data from external devices to processor and memory, and vice versa. It contains internal buffers for temporarily holding data until they can be sent on.

## Slide 9: Microprocessor
  Invention that brought about desktop and handheld computing
  Contains a processor on a single chip
  Fastest general purpose processors
  Multiprocessors
  Each chip (socket) contains multiple processors (cores)
Notes: The hardware revolution that brought about desktop and handheld computing was the invention of the microprocessor, which contained a processor on a single chip. Though originally much slower than multichip processors, microprocessors have continually evolved to the point that they are now much faster for most computations due to the physics involved in moving information around in sub-nanosecond timeframes.
Not only have microprocessors become the fastest general purpose processors available, they are now multiprocessors; each chip (called a socket) contains multiple processors (called cores), each with multiple levels of large memory caches, and multiple logical processors sharing the execution units of each core. As of 2010, it is not unusual for even a laptop to have 2 or 4 cores, each with 2 hardware threads, for a total of 4 or 8 logical processors.

## Slide 10: Graphical Processing Units (GPU’s)
  Provide efficient computation on arrays of data using Single-Instruction Multiple Data (SIMD) techniques pioneered in supercomputers
  No longer used just for rendering advanced graphics
    Also used for general numerical processing
        Physics simulations for games
        Computations on large spreadsheets
Notes: Although processors provide very good performance for most forms of computing, there is increasing demand for numerical computation. Graphical Processing Units (GPUs) provide efficient computation on arrays of data using Single-Instruction Multiple Data (SIMD) techniques pioneered in supercomputers. GPUs are no longer used just for rendering advanced graphics, but they are also used for general numerical processing, such as physics simulations for games or computations on large spreadsheets. Simultaneously, the CPUs themselves are gaining the capability of operating on arrays of data—with increasingly powerful vector units integrated into the processor architecture of the x86 and AMD64 families.
Processors and GPUs are not the end of the computational story for the modern PC.

## Slide 11: Digital Signal Processors (DSPs)
  Deal with streaming signals such as audio or video
  Used to be embedded in I/O devices like modems
      Are now becoming first-class computational devices, especially in handhelds
  Encoding/decoding speech and video (codecs)
  Provide support for encryption and security
Notes: Digital Signal Processors (DSPs) are also present, for dealing with streaming signals—such as audio or video. DSPs used to be embedded in I/O devices, like modems, but they are now becoming first-class computational devices, especially in handhelds. Other specialized computational devices (fixed function units) co-exist with the CPU to support other standard computations, such as encoding/decoding speech and video (codecs), or providing support for encryption and security.

## Slide 12: System on a Chip (SoC)
To satisfy the requirements of handheld devices, the classic microprocessor is giving way to the SoC
    Other components of the system, such as DSPs, GPUs, I/O devices (such as codecs and radios) and main memory, in addition to the CPUs and caches, are on the same chip
Notes: To satisfy the requirements of handheld devices, the classic microprocessor is giving way to the System on a Chip (SoC), where not just the CPUs and caches are on the same chip, but also many of the other components of the system, such as DSPs, GPUs, I/O devices (such as radios and codecs), and main memory.

## Slide 13: Instruction Execution
A program consists of a set of instructions stored in memory
Processor reads (fetches) instructions from memory
Processor executes each instruction
Two steps
Notes: A program to be executed by a processor consists of a set of instructions stored in memory. In its simplest form, instruction processing consists of two steps: The processor reads ( fetches ) instructions from memory one at a time and executes each instruction. Program execution consists of repeating the process of instruction fetch and instruction execution. Instruction execution may involve several operations and depends on the nature of the instruction.

## Slide 14
Notes: The processing required for a single instruction is called an instruction cycle. Using a simplified two-step description, the instruction cycle is depicted in Figure 1.2 . The two steps are referred to as the fetch stage and the execute stage. Program execution halts only if the processor is turned off, some sort of unrecoverable error occurs, or a program instruction that halts the processor is encountered.

## Slide 15: Interrupts
Mechanism by which other modules may interrupt the normal sequencing of the processor
Provided to improve processor utilization
    Most I/O devices are slower than the processor
    Processor must pause to wait for device
    Wasteful use of the processor
Notes: Virtually all computers provide a mechanism by which other modules (I/O, memory) may interrupt the normal sequencing of the processor.
Interrupts are provided primarily as a way to improve processor utilization. For example, most I/O devices are much slower than the processor. Suppose that the processor is transferring data to a printer using the instruction cycle scheme of Figure 1.2 . After each write operation, the processor must pause and remain idle until the printer catches up. The length of this pause may be on the order of many thousands or even millions of instruction cycles. Clearly, this is a very wasteful use of the processor.

## Slide 16
Table 1.1 Classes of Interrupts
Program Generated by some condition that occurs as a result of an instruction execution, such as arithmetic overflow, division by zero, attempt to execute an illegal machine instruction, and reference outside a user's allowed memory space.
Timer Generated by a timer within the processor. This allows the operating system to perform certain functions on a regular basis.
I/O Generated by an I/O controller, to signal normal completion of an operation or to signal a variety of error conditions.
Hardware Generated by a failure, such as power failure or memory
failure parity error.
Notes: Table 1.1 lists the most common classes of interrupts.

## Slide 17: Figure 1.5a Flow of Control Without Interrupts
Notes: To give a specific example, consider a PC that operates at 1 GHz, which would allow roughly 109 instructions per second. A typical hard disk has a rotational speed of 7200 revolutions per minute for a half-track rotation time of 4 ms, which is 4 million times slower than the processor.
Figure 1.5a illustrates this state of affairs. The user program performs a series of WRITE calls interleaved with processing. The solid vertical lines represent segments of code in a program. Code segments 1, 2, and 3 refer to sequences of instructions that do not involve I/O. The WRITE calls are to an I/O routine that is a system utility and that will perform the actual I/O operation. The I/O program consists of three sections:
• A sequence of instructions, labeled 4 in the figure, to prepare for the actual I/O operation. This may include copying the data to be output into a special buffer and preparing the parameters for a device command.
• The actual I/O command. Without the use of interrupts, once this command is issued, the program must wait for the I/O device to perform the requested function (or periodically check the status, or poll, the I/O device). The program might wait by simply repeatedly performing a test operation to determine if the I/O operation is done.
• A sequence of instructions, labeled 5 in the figure, to complete the operation. This may include setting a flag indicating the success or failure of the operation.
The dashed line represents the path of execution followed by the processor; that is, this line shows the sequence in which instructions are executed. Thus, after the first WRITE instruction is encountered, the user program is interrupted and execution continues with the I/O program. After the I/O program execution is complete, execution resumes in the user program immediately following the WRITE Instruction.
Because the I/O operation may take a relatively long time to complete, the I/O program is hung up waiting for the operation to complete; hence, the user program is stopped at the point of the WRITE call for some considerable period of time.

## Slide 18
Figure 1.5b
Short I/O Wait
X = interrupt occurs during course of execution of user program
Notes: With interrupts, the processor can be engaged in executing other instructions while an I/O operation is in progress. Consider the flow of control in Figure 1.5b . As before, the user program reaches a point at which it makes a system call in the form of a WRITE call. The I/O program that is invoked in this case consists only of the preparation code and the actual I/O command. After these few instructions have been executed, control returns to the user program. Meanwhile, the external device is busy accepting data from computer memory and printing it. This I/O operation is conducted concurrently with the execution of instructions in the user program.
When the external device becomes ready to be serviced, that is, when it is ready to accept more data from the processor, the I/O module for that external device sends an interrupt request signal to the processor. The processor responds by suspending operation of the current program; branching off to a routine to service that particular I/O device, known as an interrupt handler; and resuming the original execution after the device is serviced. The points at which such interrupts occur are indicated by X in Figure 1.5b . Note that an interrupt can occur at any point in the main program, not just at one specific instruction.

## Slide 19
Notes: For the user program, an interrupt suspends the normal sequence of execution. When the interrupt processing is completed, execution resumes ( Figure 1.6 ). Thus, the user program does not have to contain any special code to accommodate interrupts; the processor and the OS are responsible for suspending the user program and then resuming it at the same point.

## Slide 20
Notes: To accommodate interrupts, an interrupt stage is added to the instruction cycle, as shown in Figure 1.7 (compare Figure 1.2 ). In the interrupt stage, the processor checks to see if any interrupts have occurred, indicated by the presence of an interrupt signal. If no interrupts are pending, the processor proceeds to the fetch stage and fetches the next instruction of the current program. If an interrupt is pending, the processor suspends execution of the current program and executes an interrupt handler routine. The interrupt-handler routine is generally part of the OS. Typically, this routine determines the nature of the interrupt and performs whatever actions are needed. In the example we have been using, the handler determines which I/O module generated the interrupt and may branch to a program that will write more data out to that I/O module. When the interrupt-handler routine is completed, the processor can resume execution of the user program at the point of interruption.
It is clear that there is some overhead involved in this process. Extra instructions must be executed (in the interrupt handler) to determine the nature of the interrupt and to decide on the appropriate action. Nevertheless, because of the relatively large amount of time that would be wasted by simply waiting on an I/O operation, the processor can be employed much more efficiently with the use of interrupts.

## Slide 21: Multiple Interrupts
An interrupt occurs while another interrupt is being processed
e.g. receiving data from a communications line and printing results at the same time
Two approaches:
Disable interrupts while an interrupt is being processed
Use a priority scheme
Notes: So far, we have discussed the occurrence of a single interrupt. Suppose, however, that one or more interrupts can occur while an interrupt is being processed. For example, a program may be receiving data from a communications line and printing results at the same time. The printer will generate an interrupt every time that it completes a print operation. The communication line controller will generate an interrupt every time a unit of data arrives. The unit could either be a single character or a block, depending on the nature of the communications discipline. In any case, it is possible for a communications interrupt to occur while a printer interrupt is being processed.

## Slide 22
Notes: Two approaches can be taken to dealing with multiple interrupts. The first is to disable interrupts while an interrupt is being processed. A disabled interrupt simply means that the processor ignores any new interrupt request signal. If an interrupt occurs during this time, it generally remains pending and will be checked by the processor after the processor has reenabled interrupts. Thus, if an interrupt occurs when a user program is executing, then interrupts are disabled immediately. After the interrupt-handler routine completes, interrupts are reenabled before resuming the user program, and the processor checks to see if additional interrupts have occurred. This approach is simple, as interrupts are handled in strict sequential
order ( Figure 1.12a ).
The drawback to the preceding approach is that it does not take into account relative priority or time-critical needs. For example, when input arrives from the communications line, it may need to be absorbed rapidly to make room for more input. If the first batch of input has not been processed before the second batch arrives, data may be lost because the buffer on the I/O device may fill and overflow.
A second approach is to define priorities for interrupts and to allow an interrupt of higher priority to cause a lower–priority interrupt handler to be interrupted ( Figure 1.12b ).

## Slide 23: Memory Hierarchy
Design constraints on a computer’s memory
    How much?
    How fast?
    How expensive?
If the capacity is there, applications will likely be developed to use it
Memory must be able to keep up with the processor
Cost of memory must be reasonable in relationship to the other components
Notes: The design constraints on a computer’s memory can be summed up by three questions: How much? How fast? How expensive?
The question of how much is somewhat open ended. If the capacity is there, applications will likely be developed to use it. The question of how fast is, in a sense, easier to answer. To achieve greatest performance, the memory must be able to keep up with the processor. That is, as the processor is executing instructions, we would not want it to have to pause waiting for instructions or operands. The final question must also be considered. For a practical system, the cost of memory must be reasonable in relationship to other components.

## Slide 24: The Memory Hierarchy
Going down the hierarchy:
  Decreasing cost per bit
  Increasing capacity
  Increasing access time
  Decreasing frequency of access to the memory by the processor
Notes: The way out of this dilemma is to not rely on a single memory component or technology, but to employ a memory hierarchy . A typical hierarchy is illustrated in
Figure 1.14 . As one goes down the hierarchy, the following occur:
a. Decreasing cost per bit
b. Increasing capacity
c. Increasing access time
d. Decreasing frequency of access to the memory by the processor
Thus, smaller, more expensive, faster memories are supplemented by larger, cheaper, slower memories. The key to the success of this organization is the decreasing
frequency of access at lower levels. We will examine this concept in greater detail later in this chapter, when we discuss the cache, and when we discuss virtual
memory later in this book. A brief explanation is provided at this point.
Suppose that the processor has access to two levels of memory. Level 1 contains 1,000 bytes and has an access time of 0.1 μs; level 2 contains 100,000 bytes and has an access time of 1 μs. Assume that if a byte to be accessed is in level 1, then the processor accesses it directly. If it is in level 2, then the byte is first transferred to level 1 and then accessed by the processor. For simplicity, we ignore the time required for the processor to determine whether the byte is in level 1 or level 2.

## Slide 25: Principle of Locality
Memory references by the processor tend to cluster
Data is organized so that the percentage of accesses to each successively lower level is substantially less than that of the level above
Can be applied across more than two levels of memory
Notes: The basis for the validity of condition (d) is a principle known as locality of reference [DENN68]. During the course of execution of a program, memory references by the processor, for both instructions and data, tend to cluster. Programs typically contain a number of iterative loops and subroutines. Once a loop or subroutine is entered, there are repeated references to a small set of instructions. Similarly, operations on tables and arrays involve access to a clustered set of data bytes. Over a long period of time, the clusters in use change, but over a short period of time, the processor is primarily working with fixed clusters of memory references.
Accordingly, it is possible to organize data across the hierarchy such that the percentage of accesses to each successively lower level is substantially less than that of the level above. Consider the two-level example already presented. Let level 2 memory contain all program instructions and data. The current clusters can be temporarily placed in level 1. From time to time, one of the clusters in level 1 will have to be swapped back to level 2 to make room for a new cluster coming in to level 1. On average, however, most references will be to instructions and data contained in level 1.
This principle can be applied across more than two levels of memory. The fastest, smallest, and most expensive type of memory consists of the registers internal to the processor. Typically, a processor will contain a few dozen such registers, although some processors contain hundreds of registers. Skipping down two levels, main memory is the principal internal memory system of the computer. Each location in main memory has a unique address, and most machine instructions refer to one or more main memory addresses. Main memory is usually extended with a higher-speed, smaller cache. The cache is not usually visible to the programmer or, indeed, to the processor. It is a device for staging the movement of data between main memory and processor registers to improve performance.

## Slide 26: Cache Memory
Invisible to the OS
Interacts with other memory management hardware
Processor must access memory at least once per instruction cycle
Processor execution is limited by memory cycle time
Exploit the principle of locality with a small, fast memory
Notes: Although cache memory is invisible to the OS, it interacts with other memory management hardware. Furthermore, many of the principles used in virtual memory schemes (discussed in Chapter 8 ) are also applied in cache memory.
On all instruction cycles, the processor accesses memory at least once, to fetch the instruction, and often one or more additional times, to fetch operands and/ or store results. The rate at which the processor can execute instructions is clearly limited by the memory cycle time (the time it takes to read one word from or write one word to memory). This limitation has been a significant problem because of the persistent mismatch between processor and main memory speeds: Over the years, processor speed has consistently increased more rapidly than memory access speed. We are faced with a trade-off among speed, cost, and size. Ideally, main memory should be built with the same technology as that of the processor registers, giving memory cycle times comparable to processor cycle times. This has always been too expensive a strategy. The solution is to exploit the principle of locality by providing a small, fast memory between the processor and main memory, namely the cache.

## Slide 27
Notes: Cache memory is intended to provide memory access time approaching that of the fastest memories available and at the same time support a large memory size that has the price of less expensive types of semiconductor memories. The concept is illustrated in Figure 1.16a . There is a relatively large and slow main memory together with a smaller, faster cache memory. The cache contains a copy of a portion of main memory. When the processor attempts to read a byte or word of memory, a check is made to determine if the byte or word is in the cache. If so, the byte or word is delivered to the processor. If not, a block of main memory, consisting of some fixed number of bytes, is read into the cache and then the byte or word is delivered to
the processor. Because of the phenomenon of locality of reference, when a block of data is fetched into the cache to satisfy a single memory reference, it is likely that many of the near-future memory references will be to other bytes in the block.
Figure 1.16b depicts the use of multiple levels of cache. The L2 cache is slower and typically larger than the L1 cache, and the L3 cache is slower and typically larger than the L2 cache.

## Slide 28
Notes: Figure 1.18 illustrates the read operation. The processor generates the address, RA, of a word to be read. If the word is contained in the cache, it is delivered to the processor. Otherwise, the block containing that word is loaded into the cache and the word is delivered to the processor.

## Slide 29: Symmetric Multiprocessors (SMP)
A stand-alone computer system with the following characteristics:
  Two or more similar processors of comparable capability
  Processors share the same main memory and are interconnected by a bus or other internal connection scheme
  Processors share access to I/O devices
  All processors can perform the same functions
  The system is controlled by an integrated operating system that provides interaction between processors and their programs at the job, task, file, and data element levels
Notes: An SMP can be defined as a stand-alone computer system with the following characteristics:
1. There are two or more similar processors of comparable capability.
2. These processors share the same main memory and I/O facilities and are interconnected by a bus or other internal connection scheme, such that memory access time is approximately the same for each processor.
3. All processors share access to I/O devices, either through the same channels or through different channels that provide paths to the same device.
4. All processors can perform the same functions (hence the term symmetric ).
5. The system is controlled by an integrated operating system that provides interaction between processors and their programs at the job, task, file, and
data element levels.
Points 1 to 4 should be self-explanatory. Point 5 illustrates one of the contrasts with a loosely coupled multiprocessing system, such as a cluster. In the latter, the physical unit of interaction is usually a message or complete file. In an SMP, individual data elements can constitute the level of interaction, and there can be a high degree of cooperation between processes.

## Slide 30
Notes: Figure 1.19 illustrates the general organization of an SMP.
There are multiple processors, each of which contains its own control unit, arithmetic logic unit, and registers. Each processor has access to a shared main memory and the I/O devices through some form of interconnection mechanism; a shared bus is a common facility. The processors can communicate with each other through memory (messages and status information left in shared address spaces). It may also be possible for processors to exchange signals directly. The memory is often organized so that multiple simultaneous accesses to separate blocks of memory are possible.
In modern computers, processors generally have at least one level of cache memory that is private to the processor. This use of cache introduces some new design considerations. Because each local cache contains an image of a portion of main memory, if a word is altered in one cache, it could conceivably invalidate a word in another cache. To prevent this, the other processors must be alerted that an update has taken place. This problem is known as the cache coherence problem and is typically addressed in hardware rather than by the OS.

## Slide 31: SMP Advantages
Performance
A system with multiple processors will yield greater performance if work can be done in parallel
Availability
The failure of a single processor does not halt the machine
Incremental Growth
An additional processor can be added to enhance performance
Scaling
Vendors can offer a range of products with different price and performance characteristics
Notes: An SMP organization has a number of potential advantages over a uniprocessor organization, including the following:
• Performance: If the work to be done by a computer can be organized so that some portions of the work can be done in parallel, then a system with multiple processors will yield greater performance than one with a single processor of the same type.
Availability: In a symmetric multiprocessor, because all processors can perform the same functions, the failure of a single processor does not halt the machine. Instead, the system can continue to function at reduced performance.
• Incremental growth: A user can enhance the performance of a system by adding an additional processor.
• Scaling: Vendors can offer a range of products with different price and performance characteristics based on the number of processors configured in the system.
It is important to note that these are potential, rather than guaranteed, benefits. The operating system must provide tools and functions to exploit the parallelism in an SMP system. An attractive feature of an SMP is that the existence of multiple processors is transparent to the user. The operating system takes care of scheduling of tasks on individual processors and of synchronization among processors.

## Slide 32: Multicore Computer
Also known as a chip multiprocessor
Combines two or more processors (cores) on a single piece of silicon (die)
    Each core consists of all of the components of an independent processor
In addition, multicore chips also include L2 cache and in some cases L3 cache
Notes: A multicore computer, also known as a chip multiprocessor , combines two or more processors (called cores) on a single piece of silicon (called a die). Typically, each core consists of all of the components of an independent processor, such as registers, ALU, pipeline hardware, and control unit, plus L1 instruction and data caches. In addition to the multiple cores, contemporary multicore chips also include L2 cache and, in some cases, L3 cache.
The motivation for the development of multicore computers can be summed up as follows. For decades, microprocessor systems have experienced a steady, usually exponential, increase in performance. This is partly due to hardware trends, such as an increase in clock frequency and the ability to put cache memory closer to the processor because of the increasing miniaturization of microcomputer components. Performance has also been improved by the increased complexity of processor design to exploit parallelism in instruction execution and memory access. In brief, designers have come up against practical limits in the ability to achieve greater performance by means of more complex processors. Designers have found that the best way to improve performance to take advantage of advances in hardware is to put multiple processors and a substantial amount of cache memory on a single chip. A detailed discussion of the rationale for this trend is beyond our scope, but is summarized in Appendix C .

## Slide 33
Notes: An example of a multicore system is the Intel Core i7-5960X, which includes
six x86 processors, each with a dedicated L2 cache, and with a shared L3 cache
(Figure 1.20a). One mechanism Intel uses to make its caches more effective is
prefetching, in which the hardware examines memory access patterns and attempts to
fill the caches speculatively with data that’s likely to be requested soon. Figure 1.20b
shows the physical layout of the 5960X in its chip.
The Core i7-5960X chip supports two forms of external communications to
other chips. The DDR4 memory controller brings the memory controller for the
DDR (double data rate) main memory onto the chip. The interface supports four
channels that are 8 bytes wide for a total bus width of 256 bits, for an aggregate data
rate of up to 64 GB/s. With the memory controller on the chip, the Front Side Bus is
eliminated. The PCI Express is a peripheral bus. It enables high-speed communications
among connected processor chips. The PCI Express link operates at 8 GT/s
(transfers per second). At 40 bits per transfer, that adds up to 40 GB/s.

## Slide 34: Summary
Basic Elements
Instruction execution
Interrupts, Interrupt processing, Multiple interrupts
The memory hierarchy
Cache memory: principles and design
Multiprocessor and multicore organization
Notes: A multicore computer, also known as a chip multiprocessor , combines two or more processors (called cores) on a single piece of silicon (called a die). Typically, each core consists of all of the components of an independent processor, such as registers, ALU, pipeline hardware, and control unit, plus L1 instruction and data caches. In addition to the multiple cores, contemporary multicore chips also include L2 cache and, in some cases, L3 cache.
The motivation for the development of multicore computers can be summed up as follows. For decades, microprocessor systems have experienced a steady, usually exponential, increase in performance. This is partly due to hardware trends, such as an increase in clock frequency and the ability to put cache memory closer to the processor because of the increasing miniaturization of microcomputer components. Performance has also been improved by the increased complexity of processor design to exploit parallelism in instruction execution and memory access. In brief, designers have come up against practical limits in the ability to achieve greater performance by means of more complex processors. Designers have found that the best way to improve performance to take advantage of advances in hardware is to put multiple processors and a substantial amount of cache memory on a single chip. A detailed discussion of the rationale for this trend is beyond our scope, but is summarized in Appendix C .